RSP2 Response

Wes and Jim,

After a lot of flailing around and some help from Nathan I think I have found some settings for the RSP2 (and probably the RSP1 as well).  As you can see from the curve below the dynamic range for the machine itself is close to 40 dB.

Make the following settings without regard for where the color gain and color offset of RSS are set.  This insures that the RSP itself has a good dynamic range.

Use the following settings:

LOG Scale (under integrate) ON

Gain Reduction 25

Offset 41.220

Gain 0.015

The following plot shows the output mv in RSS (voltmeter) vs the attenuation in dB of the Kay attenuator placed between the HP461 and the RSP2.

Adjusting the RSS color gain and offset.

Solar

If you want to achieve the full color dynamic range of the RSP for solar work then the color should go into red saturation at about the same time the instrument itself goes into saturation (4000 mv), and the color should be deep blue on the galactic background.  To achieve this, set your RSS color offset to (0) and the color gain to (1.5).  Don’t change any of the RSP2/1 controls.

Response for full dynamic range solar observations (numbers are dB of atten and temp)

Jupiter

Since Jupiter signals are much weaker than strong solar bursts it is sufficient to have about a 20 dB dynamic range of colors.  This means increasing the RSS color gain to 3 and the color offset to 200.  Don’t change any of the RSP2/1 controls.

Response for 20 dB dynamic range for Jupiter (numbers are dB of atten and temp)

Please try these settings – they should be good for the TFD array.  Let me know how they work. Please do not distribute this paper.  Need to verify that it is right.

Dick